## Slide 1: Capstone Project:
A novel, real-time step counting algorithm
Henry Valk

## Slide 2: Step Counting: Current Methods
Common Methods
  Windowed peak detection
    Pros: computationally inexpensive
    Cons: susceptible to false positives
Academic Research
  Template Based (DTW, Wavelet)
  Frequency Based (autocorrelation, FFT)
  Feature-Based Neural Networks
    Pros: highly accurate
    Cons: computationally expensive, can require massive amount of training data
Accelerometer: measures linear acceleration (m/sec2)
Gyroscope: measures angular velocity (degrees/sec)

## Slide 3: Proposed Algorithm
Goals
  Better accuracy than peak detection
  Considers computational efficiency
  Remains white-box / intuitive / parameter-light
Frequency-Based Walk Detection
Accelerometer Z
Walking
no
0.5 sec interval
yes
no
yes
Template-Based
Step Counter
Step
yes
Increment step count

## Slide 4: Brajdic & Harle 2013 Walking Dataset
Smartphone accelerometer data from 27 participants (23 used here)
Data gathered with smartphone in 6 positions (“handheld / not-in-use” used as a proxy for a wrist-worn device)
Total steps and walking onset / offset timestamps recorded, however individual step timestamps unknown

## Slide 5: UbiComp Sample Data
Samples
Linear Acceleration (m/sec2)

## Slide 6: Frequency-Based Walk Detection
Most people walk with a stride rate between 1.2 and 2.4 hz
By transforming the accelerometer signal from the time domain to the frequency domain, we can assess whether the incoming signal shows a stride rate consistent with walking

## Slide 7: Fourier Transform

## Slide 8: Fourier Transform
2 hz
6 hz
3 hz

## Slide 9: Fourier Transform
FFT
2 hz
6 hz
3 hz
2 hz
3 hz
6 hz

## Slide 10: Frequency-Based Walk Detection
If sample_count >= 250 and sample_count % 50 == 0:
if FT(last250samples, 1.2 : 2.4) > FT(last250samples,0 : 1.2) and FT(last250samples, 1.2 : 2.4) > threshold:
walking = True
else:
walking = False
Kang, X., Huang, B., & Qi, G. (2018). A Novel Walking Detection and Step Counting Algorithm Using Unconstrained Smartphones. Sensors (Basel, Switzerland), 18(1), 297. https://doi.org/10.3390/s18010297
1.2 hz
2.4 hz
Binned Power Spectrum Density

## Slide 11: Offline Walk Detection Performance
Specificity | 0.7235
Sensitivity | 0.9946

## Slide 12
Frequency-Based Walk Detection
Template-Based
Step Counter
Accelerometer Z
Walking
Step
no
0.5 sec interval
yes
no
yes
yes
Increment step count

## Slide 13: Template-Based Step Counter
Comparing incoming data to an ideal step or average step template
A = [1,1,3,5,6,6,5,4,3,1,2,2,2,4,5]
B = [1,1,1,2,4,4,5,7,7,5,4,3,3,2,2,3,5,5,6]

## Slide 14: Template-Based Step Counter
Comparing incoming data to an ideal step or average step template
A = [1,1,3,5,6,6,5,4,3,1,2,2,2,4,5]
B = [1,1,1,2,4,4,5,7,7,5,4,3,3,2,2,3,5,5,6]

## Slide 15: Dynamic Time Warping

## Slide 16: Dynamic Time Warping
DTW(i,j) = d(Ai ,Bj ) + min{ DTW(i-1,j-1), …………………………......…DTW(i-1,j ), ……………………....…..……DTW(i,j-1)}
A
B

## Slide 17: Dynamic Time Warping
DTW(i,j) = d(Ai ,Bj ) + min{ DTW(i-1,j-1), …………………………......…DTW(i-1,j ), ……………………....…..……DTW(i,j-1)}
A
B

## Slide 18: Dynamic Time Warping
DTW(i,j) = d(Ai ,Bj ) + min{ DTW(i-1,j-1), …………………………......…DTW(i-1,j ), ……………………....…..……DTW(i,j-1)}
DTW(i,j) = abs(3-4) + min{ 4, ………………………….....…7, ……………………..,......……2}
DTW(i,j) = 1 + 2 = 3
A
B

## Slide 19: Dynamic Time Warping

## Slide 20: Dynamic Time Warping

## Slide 21: Dynamic Time Warping

## Slide 22: Dynamic Time Warping

## Slide 23: Dynamic Time Warping

## Slide 24: Dynamic Time Warping

## Slide 25: Dynamic Time Warping

## Slide 26: Dynamic Time Warping

## Slide 27: Dynamic Time Warping

## Slide 28: DTW SPRING
Yasushi Sakurai, Christos Faloutsos, Masashi Yamamuro: Stream Monitoring under the Time Warping Distance. ICDE 2007:1046-1055
Image: Abdullah Mueen, Eamonn J. Keogh: Extracting Optimal Performance from Dynamic Time Warping. KDD 2016: 2129-2130

## Slide 29: Step Template
Mean step from 23 participants in UbiComp dataset
Approximately 1.8hz stride rate

## Slide 30: Sample Step Counting
DTW SPRING with step template and UbiComp walking data

## Slide 31: Offline Step Count Accuracy
True Step Count | Steps Counted | % Error
74 | 64 | 0.13513514
85 | 79 | 0.07058824
... | ... | ...
85 | 70 | 0.17647059
70 | 64 | 0.08571429
Overall Accuracy: 87.16%

## Slide 32: MbientLab MetaMotionR
100hz sampling rate
Accelerometer, gyro, magnetometer, temperature, barometer
Stream via Bluetooth LE

## Slide 33: MetaWear API
Python3 API that wraps around the MetaWear C++ library
Supported on Linux
All development done in VirtualBox virtual machine running latest Ubuntu

## Slide 35: Limitations and Future Directions
Write code in Swift and run from a mobile app
Save output to CSV file
Measure ground truth step count for more accurate algorithm evaluation
Replicate algorithm for running, walking down stairs, etc
Fine tuning:
  Compare accuracy at different sampling rates
  Try multidimensional DTW SPRING

## Slide 36: Thank you!
Yasushi Sakurai, Christos Faloutsos, Masashi Yamamuro: Stream Monitoring under the Time Warping Distance. ICDE 2007:1046-1055
Abdullah Mueen, Eamonn J. Keogh: Extracting Optimal Performance from Dynamic Time Warping. KDD 2016: 2129-2130
Kang, X., Huang, B., & Qi, G. (2018). A Novel Walking Detection and Step Counting Algorithm Using Unconstrained Smartphones. Sensors (Basel, Switzerland), 18(1), 297. https://doi.org/10.3390/s18010297
Harle, R., & Brajdic, A. (2017). Research data supporting "Walk detection and step counting on unconstrained smartphones" [Dataset]. https://doi.org/10.17863/CAM.12982
Shokoohi-Yekta, M., Hu, B., Jin, H., Wang, J., & Keogh, E. (2017). Generalizing DTW to the multi-dimensional case requires an adaptive approach. Data mining and knowledge discovery, 31(1), 1–31. https://doi.org/10.1007/s10618-016-0455-0
Nikolas Rieble - https://stackoverflow.com/questions/36549932/pattern-detection-in-time-series-data
http://scipy.github.io/devdocs/generated/scipy.signal.welch.html
https://mbientlab.com/tutorials/CppDevelopment.html